## Slide 1: 第三章书面作业

## Slide 2: Exercise 3.16
Determine the DTFT of each of the following sequences:
(a)
(c)
(e)

## Slide 3: Exercise 3.60
A 4.0s long segment of a continuous-time signal is uniformly sampled without aliasing and generating a finite-length sequence containing 8500 samples. What is the highest frequency component that could be present in the continuous-time signal?

## Slide 4: Exercise 3.61
A continuous-time signal x(t) is composed of a linear combination of sinusoidal signals of frequencies 300Hz, 500Hz, 1.2kHz, 2.15kHz, and 3.5kHz. The signal x(t) is sampled at a 3.0-kHz rate, and the sampled sequence is passed an ideal lowpass filter with a cutoff frequency of 900Hz, generating a continuous-time signal y(t). What are the frequency components present in the reconstructed signal y(t)?